## Slide 1: ST Competitors Benchmark STEP2 MW stacks performance
April 22nd, 2026
STM32Cube Support & Maintenance Team (Tunis)

## Slide 2: Agenda
1
Tests plan
2
Summary & Next steps
3
RTOS Middleware
4
File System Middleware
5
USB Middleware
6
Continuation Plan Proposal

## Slide 3: ST vs Competitors MW Benchmark: Tests Plan

## Slide 4: ST vs Competitors MW Benchmark: Tests Plan
 | TI | Renesas | NXP
USB | NA due to STM32C0 and MSPM0 (low end products) hardware limitations | MW stack: AzureRTOS USBX 6.4.0 MCUs: STM32H573I-DK vs EK-RA6M5 Use Cases: 1- RTOS mode: HID host class 2- RTOS mode: CDC device class 3- RTOS mode: MSC host class | MW stack: STM32/NXP native USB Library Due to Microsoft discontinuation of Azure RTOS, the NXP SDK package supports no more Azure RTOS after version 2.15. MCUs: STM32U575xx vs MCX-N9 Use Cases: 1- BareMetal mode: HID device class 2- BareMetal mode: CDC device class 3- BareMetal mode: MSC host class
File System | NA due to STM32C0 and MSPM0 (low end products) hardware limitations | MW stack: AzureRTOS FileX 6.4.0 MCUs: STM32H573I-DK vs EK-RA6M5 Use Cases: 1- BareMetal mode: FileX w/ SRAM internal memory 2- RTOS mode: FileX w/ USB disk memory | MW stack: FatFS V R0.15 Due to Microsoft discontinuation of Azure RTOS, the NXP SDK package supports no more Azure RTOS after version 2.15. MCUs: STM32U575xx vs MCX-N9 Use Cases: 1- BareMetal mode: FatFS w/ SRAM internal memory 2- BareMetal mode: FatFS w/ SD card
RTOS | MW/Version: FreeRTOS 10.6.2 MCUs: STM32C031C6 vs TI MSPM0G3507 Use Cases: 1- Basic Processing Test 2- Cooperative Scheduling Test 3- Preemptive Scheduling Test | MW stack: AzureRTOS ThreadX 6.4.0 MCUs: STM32H573I-DK vs EK-RA6M5 Use Cases: 1- Basic Processing Test 2- Cooperative Scheduling Test 3- Preemptive Scheduling Test | Due to Microsoft discontinuation of Azure RTOS, the NXP SDK package supports no more Azure RTOS after version 2.15.
 | TI does not support AzureRTOS | MW stack: FreeRTOS 10.6.2 MCUs: STM32H743I-EVAL vs EK-RA8M1 Use Cases: 1- Basic Processing Test 2- Cooperative Scheduling Test 3- Preemptive Scheduling Test | MW stack: FreeRTOS 11.1.0 MCUs: STM32U575xx vs MCX-N9 Use Cases: 1- Basic Processing Test 2- Cooperative Scheduling Test 3- Preemptive Scheduling Test
Footprint and Execution time measures are performed on mentioned tests

## Slide 5: Summary & Next steps

## Slide 6: ST Competitors MW Benchmark: Footprint summary
FreeRTOS V10.6.2(TI/Renesas) V11.1.0 (NXP) Footprint
File System FatFS R0.15 Footprint
USB Native Library Footprint
TI and NXP does not support AzureRTOS ThreadX
TI MSPM0G3507 board does not support USB peripheral
NXP does not support AzureRTOS USBX
TI software package does not support File System Library
NXP does not support AzureRTOS FileX
AzureRTOS ThreadX V6.4.0 Footprint
AzureRTOS FileX V6.4.0 Footprint
 | ST vs TI | ST vs RA | ST vs NXP
CDC device class (BareMetal) | NA | NA | +34%
HID Device Class (BareMetal) |  |  | +21%
MSC Host Class (BareMetal) |  |  | +27%
AzureRTOS USBX V6.4.0 Footprint
 | ST vs TI | ST vs RA | ST vs NXP
CDC Device Class (RTOS) | NA | -51% | NA
HID Host Class (RTOS) |  | -40% | 
MSC Host Class (RTOS) |  | -11% | 
 | ST vs TI | ST vs RA | ST vs NXP
Internal SRAM Test (BareMetal) | NA | Not Done | -82%
SD card Test (BareMetal) |  |  | +4%
 | ST vs TI | ST vs RA | ST vs NXP
Basic Processing Test | +17% | -68% | -2%
Cooperative Processing Test | +13% | -41% | +6%
Preemptive Processing Test | +15% | -73% | +8%
 | ST vs TI | ST vs RA | ST vs NXP
Basic Processing Test | NA | -45% | NA
Cooperative Processing Test |  | -46% | 
Preemptive Processing Test |  | -45% | 
TI MSPM0G3507 board does not support USB peripheral
* TI software package does not support File System Library
Renesas uses more complex structures in HAL&RM layers and sets more data variables, which improves code readability but increases RAM usage.
NXP’s fsl_ram_disk.h allocate max RAM size for buffer disk_space (95 KB)
Renesas uses more complex structures in HAL&RM (Renesas Middleware) layers and sets more data variables, which improves code readability but increases RAM usage.
Ratio = ((ST - Compet) / Compet)*100
Used HW boards:
TI: STM32C031C6 vs TI MSPM0G3507
RA: STM32H573 vs EK-RA6M5/ STM32H743 vs EK-RA8M1
NXP: STM32U575xx vs MCX-N9
IDE:
EWARM 9.60.3
Tools:
Data Watchpoint (DWT)/
LeCroy USB analyzer
STM32U5 footprint overhead is coming mainly from HAL RCC configuration, not from USB stack
 | ST vs TI | ST vs RA | ST vs NXP
Internal SRAM Test (baremetal) | NA | -32% | NA
USB Disk Test (RTOS) |  | -26% | 
Due to STM32C0 clock configuration (HAL_RCC_ClockConfig() API).

## Slide 7: ST Competitors MW Benchmark: Execution Time summary
Ratio = ((ST - Compet) / Compet)*100
Used HW boards:
TI: STM32C031C6 vs TI MSPM0G3507
RA: STM32H573 vs EK-RA6M5/ STM32H743 vs EK-RA8M1
NXP: STM32U575xx vs MCX-N9
IDE:
EWARM 9.60.3
Tools:
Data Watchpoint (DWT)/
LeCroy USB analyzer
 |  | ST vs TI | ST vs RA | ST vs NXP
Internal SRAM Test (Baremetal) | Init | NA | -22% | NA
 | create |  | -9% | 
 | write |  | -9% | 
 | read |  | -33% | 
USB Disk Test (RTOS) | Init | NA | -29% | NA
 | create |  | +88% | 
 | write |  | +41% | 
 | read |  | +2% | 
File System FatFS R0.15 Execution Time
USB Native Library Execution Time
AzureRTOS ThreadX V6.4.0 Performance
AzureRTOS FileX V6.4.0 Execution Time
 |  | ST vs TI | ST vs RA | ST vs NXP
CDC Device Class (BareMetal) | Init | NA | Not Done | +22%
 | Enumeration |  |  | +2%
 | Transmit |  |  | -1%
 | Receive |  |  | 0%
HID Device Class (BareMetal) | Init | NA | Not Done | +100%
 | Enumeration |  |  | -1%
 | Data transmission |  |  | 0%
MSC Host Class (BareMetal) | Init | NA | Not Done | +12%
 | Enumeration |  |  | -18%
 | Write |  |  | -2.7%
 | Read |  |  | -3%
AzureRTOS USBX V6.4.0 Execution Time
 |  | ST vs TI | ST vs RA | ST vs NXP
Internal SRAM Test (BareMetal) | Init | NA | Not Done | +37%
 | create |  |  | +7%
 | write |  |  | -7%
 | read |  |  | +2%
SD Card Test (BareMetal) | Init | NA | Not Done | -41%
 | create |  |  | -99%
 | write |  |  | -89%
 | read |  |  | -3%
 | ST vs TI | ST vs RA | ST vs NXP
Basic Processing Test (Thread/s) | -0.45% | -9% | -0,09%
Cooperative Processing Test (Thread/30s) | +6% | +31% | +8%
Preemptive Processing Test (Thread/30s) | +1% | -1% | +4%
 | ST vs TI | ST vs RA | ST vs NXP
Basic Processing Test (Thread/s) | NA | +19% | NA
Cooperative Processing Test (Thread/30s) |  | +16% | 
Preemptive Processing Test (Thread/30s) |  | +17% | 
 |  | ST vs TI | ST vs RA |  | ST vs NXP
CDC Device Class (RTOS) | Init | NA | -95% |  | 
 | Enumeration |  | -2% |  | 
 | Transmit |  | -1% |  | 
 | Receive |  | 0% |  | 
HID Host Class (RTOS) | Init | NA | -51% |  | NA
 | Enumeration |  | +650% |  | 
 | Data transmission |  | -5.6% |  | 
MSC Host Class (RTOS) | Init | NA | -56% |  | NA
 | Enumeration |  | +950% |  | 
 | Write |  | -33% | 0% | 
 | Read |  | -64% | +15% | 
STM32 waits a delay of 50 ms (defined in USBX) after device setting vs RA handles enumeration in rm_usbx_ports layer (no delay)
STM32 SD HAL driver performing better than NXP
* TI MSPM0G3507 board does not support USB peripheral
* NXP does not support AzureRTOS USBX
* USBX supports BareMetal mode from 6.11.0 version (link)
stm32h5xx_hal_hcd.c / HCD_HC_IN_IRQHandler() static function enhancement request submitted
Bugzilla Ticket 217913
* TI MSPM0 Library does not support FatFS/FileX
* NXP does not support AzureRTOS FileX
*TI and NXP does not support AzureRTOS ThreadX
Throughput (KB/s): the higher the better
Throughput (KB/s): the higher the better
FreeRTOS V10.6.2(TI/Renesas) V11.1.0 (NXP) Performance
* RTOS performance is evaluated by context switching rate metric (thread/s): The higher the better

## Slide 8: Continuation Plan Proposal
Middleware Stack | Benchmark Scope | HW Board | 
STM32 vs Renesas |  |  | 
FreeRTOS | Low-footprint multitasking efficiency: task lifecycle cost, API latency, context-switch overhead | FPB-RA0E1 vs NUCLEO-STM32L031 | FPB-RA0E1 vs NUCLEO-STM32L031
LevelX | Persistent storage efficiency and flash-management readiness: format, mount/remount, small-file create/delete | EK-RA8M1 vs STM32H753 | EK-RA8M1 vs STM32H753
USB | USB stack footprint and class initialization performance: CDC, HID, MSC | FPB-RA8E1 vs NUCLEO-STM32H743 | FPB-RA8E1 vs NUCLEO-STM32H743
STM32 vs NXP |  |  | 
FreeRTOS | Low-power RTOS efficiency: task management, synchronization, queues, timers, wakeup/sleep transitions, context-switch latency | FRDM-MCXA156 vs NUCLEO-L552ZE-Q | FRDM-MCXA156 vs NUCLEO-L552ZE-Q
FatFS | SD storage middleware efficiency: mount, format, file operations, directory scan | MIMXRT1060-EVKV vs STM32H735G-DK | MIMXRT1060-EVKV vs STM32H735G-DK
USB Device | USB FS device stack efficiency across CDC, HID, MSC: initialization, enumeration, control-transfer, transfer performance | FRDM-MCXA156 vs NUCLEO-L552ZE-Q | FRDM-MCXA156 vs NUCLEO-L552ZE-Q
LwIP | Ethernet stack efficiency: startup, network service latency, socket performance, TCP/UDP throughput | MIMXRT1060-EVKC vs STM32H735G-DK | MIMXRT1060-EVKC vs STM32H735G-DK
STM32 vs GigaDevice |  |  | 
USB Device | Measure USB device stack efficiency across HID, CDC, and MSC through footprint, initialization, enumeration, and transfer performance. | GD32E507Z-EVAL vs STM32U5A9J-DK | GD32E507Z-EVAL vs STM32U5A9J-DK
FreeRTOS | Measure RTOS responsiveness and scalability through task, sync, queue, timer, ISR wakeup, and context-switch performance. |  | 
FatFS | Measure file-system efficiency on external and removable storage through mount, format, and file operation performance. |  | 
LwIP | Measure Ethernet stack efficiency through startup, network service latency, socket performance, and TCP/UDP throughput. |  | 

## Slide 9: ST Competitors MW Benchmark: RTOS Objective Performance comparison
This benchmark analysis was based on a series of tests from the Thread Metric benchmark suite, formerly offered by Microsoft and now offered by the Eclipse Foundation(*). The Thread Metric benchmark suite is under MIT license and can be found on GitHub here: Thread Metric Benchmark Suite.
The Thread Metric benchmark suite consists of eight tests, For this study, we have selected the following three Thread Metric RTOS performance tests:
Basic Processing: The test uses two threads: a low-priority counting thread that continuously updates a global counter, and a high-priority reporting thread that sleeps for 30 seconds before reporting the counter difference to monitor system performance.
Cooperative Processing: The test runs with six threads: five cooperative threads of equal priority that yield control before incrementing their counters, and one high-priority reporting thread that sleeps for 30 seconds before reporting the counters.
Preemptive Scheduling: The test runs with six threads: five preemptive threads with ascending priorities where each resumes the next higher-priority thread before incrementing its counter and suspending itself (except the lowest-priority thread), and a high-priority reporting thread that sleeps for 30 seconds before reporting the counters.
These performed analyses are in line with the defined test plan in slide2
(*) Source: white paper available at RTOS 2024 Performance Report

## Slide 10: ST Competitors MW Benchmark: RTOS Flowcharts
Clock frequency: TI:48MHz , NXP:150MHz , Renesas:200MHz
Start
Clock configuration
LOW Priority
Create Counting Thread
Create Reporting Thread
Start the scheduler
Initialize a global counter to 0
1 ms time slice/task
Start Counting Thread
Initialize an array to 0
Update array elements
Increment the global counter
Start Reporting Thread
Initialize last_counter to 0
Sleep for 30 s
Print :global counter – last counter
HIGH Priority
counter holding previous
Counter value
Thread blocked for 30s and only
Thread0 runs and loop back again
To sleep for 30s
Basic Processing Flowchart
HIGH Priority
Clock configuration
Create 5 threads
Create Reporting Thread
Start the scheduler
Initialize 5 global counters to 0
Start Thread i
Task Yield
Increment Ci
Start
Start Thread i+1
Task Yield
Increment Ci+1
i+1 = 4
i+1 = 4
Clock frequency: TI:48MHz , NXP:150MHz , Renesas:480MHz
c0 to c4
same low priority
1 ms time slice/task
Cooperative Processing Flowchart
Start Reporting Thread
Sleep for 30 s
Print the 5 counters
HIGH Priority
Clock configuration
Create 5 threads
Create Reporting Thread
Suspend thread 1,2,3,4
Initialize 5 global counters to 0
Start Thread i
Resume thread i
Increment Ci
Start
Start Thread i+1
Resume thread i+1
Increment Ci+1
To Next thread
From Next thread
Clock frequency: TI:48MHz , NXP:150MHz , Renesas:200MHz
c0 to c4
ascending priorities ,from lowest to highest
Suspend Threads 1 through 4 ;start with Thread 0 active
Suspend Ci+1
Preemptive Scheduling Flowchart
Start Reporting Thread
Sleep for 30 s
Print the 5 counters

## Slide 11: ST Competitors MW Benchmark: RTOS ST vs TI, NXP & Renesas Tests
FreeRTOS performance (thread/s)
FreeRTOS 10.6.2 (TI/ Renesas)
FreeRTOS 11.1.0 (NXP)
AzureRTOS ThreadX 6.4.0
ThreadX performance (thread/s)
FreeRTOS Footprint
ThreadX Footprint
ST vs TI: Almost the same FreeRTOS performance, but, ST has slightly higher footprint due to STM32C0 clock configuration (HAL_RCC_ClockConfig() API).
ST vs RA: ST has better performance in cooperative processing, and better footprint consumption than Renesas (RA uses more complex data structures).
ST vs NXP: Close FreeRTOS performance and footprint consumption between ST and NXP.
ST vs RA: ST has better performance in basic, cooperative and preemptive processing, and better footprint consumption than Renesas (RA uses more complex data structures).
TI and NXP does not support AzureRTOS.
 | ST vs TI |  |  | ST vs RA |  |  | ST vs NXP |  | 
 | STM32C031 (CM0) | MSPM0 (CM0) | ST vs TI | STM32H753 (CM7) | RA8M1 (CM85) | ST vs RA | STM32U57 (CM33) | MCX-N9 (CM33) | ST vs NXP
Basic Processing Test (Thread/s) | 11 601 | 11 654 | -0.45% | 371 403 | 409 858 | -9% | 44 935 | 44 976 | -0,09%
Cooperative Processing Test (Thread/30s) | 1 487 998 | 1 384 372 | +6% | 18 386 498 | 14 033 811 | +31% | 7 246 282 | 6 662 997 | +8%
Preemptive Processing Test (Thread/30s) | 401 408 | 396 327 | +1% | 5414999 | 5444699 | -1% | 1 688 749 | 1 615 521 | +4%
 | ST vs TI |  |  | ST vs RA |  |  | ST vs NXP |  | 
 | STM32C031 (CM0) | MSPM0 (CM0) | ST vs TI | STM32H753 (CM7) | RA8M1 (CM85) | ST vs RA | STM32U57 (CM33) | MCX-N9 (CM33) | ST vs NXP
Basic Processing Test (Thread/s) | NA | NA | NA | 40 608 | 33 886 | +19% | NA | NA | NA
Cooperative Processing Test (Thread/30s) | NA | NA | NA | 4 539 885 | 4 039 910 | +16% | NA | NA | NA
Preemptive Processing Test (Thread/30s) | NA | NA | NA | 2 001 661 | 1 697 061 | +17% | NA | NA | NA
Test | Footprint | ST vs TI | ST vs RA | ST vs NXP
Basic Processing | ROM | +4% | -92% | 0%
 | RAM | +14% | -84% | +2%
 | Total | +17% | -68% | -2%
Cooperative Processing | ROM | +5% | -89% | +10%
 | RAM | +12% | -43% | +1%
 | Total | +13% | -41% | +6%
Preemptive Processing | ROM | +19% | -28% | +8%
 | RAM | +13% | +99% | +4%
 | Total | +15% | -73% | +8%
Test | Footprint | ST vs TI | ST vs RA | ST vs NXP
Basic Processing | ROM | NA | 0% | NA
 | RAM | NA | -68% | NA
 | Total | NA | -45% | NA
Cooperative Processing | ROM | NA | +12% | NA
 | RAM | NA | -69% | NA
 | Total | NA | -46% | NA
Preemptive Processing | ROM | NA | -34% | NA
 | RAM | NA | -64% | NA
 | Total | NA | -45% | NA

## Slide 12: ST Competitors MW Benchmark: File System Objective Performance comparison
This benchmark analysis was based on projects available within the ST, Renesas, and NXP firmware packages. Some updates were made in the applications to align with the scenario, memory type, and target series.
Test | Test Description | Reference project
BareMetal mode: Filex w/ SRAM internal memory STM32H743xx (CM7) vs RA8M1 (CM85) | The test allows to assess the AzureRTOS FILEX file system operations on SRAM internal memory as a storage space. File system operations to be analyzed are: File: Initialize, Create , write, read | ST: STM32U5G9J-DK2\Applications\FileX\Fx_File_Edit_Standalone
 |  | RA: baremetal_ek_ra8m1 (available in ra8m1-example)
RTOS mode: Filex w/ USB disk memory STM32H573xx (CM33) vs RA6M5 (CM33) | The test allows to assess the AzureRTOS FILEX file system operations on USB disk as a storage space. File system operations to be analyzed are: File: Initialize, Create , write and read | ST: STM32U575I-EV\Applications\USBX\Ux_Host_MSC
 |  | RA: USBX_hmsc_ek_ra6m5_ep (available in ra6m5-example)
BareMetal mode: FatFS w/ SRAM internal memory STM32U575xx (CM33) vs MCX-N9 XX (CM33) | The test allows to assess the FatFS file system operations on SRAM internal memory as a storage space. File system operations to be analyzed are: FatFS initialization, File creation, read and write. | ST: STM32469I_EVAL/Applications/FatFs/FatFs_RAMDisk
 |  | NXP: mcxn9xxevk\sdmmc_examples\sdcard_fatfs
BareMetal mode: FatFS w/ SD card STM32U575xx (CM33) vs MCX-N9 XX (CM33) | The test allows to assess the FatFS file system operations on SD card as a storage space. File system operations to be analyzed are: FatFS initialization, SD card initialization, File creation, read and write | ST: NUCLEO-H743ZI\Applications\FatFS\FatFS_uSD_Standalone
 |  | NXP: mcxn9xxevk\sdmmc_examples\sdcard_fatfs
Renesas
NXP
These performed analyses are in line with the defined test plan in slide2

## Slide 13: ST Competitors MW Benchmark: File System ST vs Renesas Flowcharts
Clock frequency: 480 MHz (ST and Renesas)
Clock source : HSI RC (ST) / PLL (Renesas)
fx_ram_driver
Clock configuration
Filex initilize
Format and open media
End
Create the file
Write in the file
Read the file
Close the file
Start
date & time, sector cache, Fat cache size, Filex libraries
BareMetal mode: Filex w/ SRAM internal memory
STM32H743xx (CM7) vs RA8M1 (CM85)
Clock configuration
RTOS Kernel Start
Filex Init
USBx Init
USB Host, MSC class, power USB module
Create the file
Write in file
Close the file
Read the file
Is USB flash inserted ?
Yes
No
USB enumeration
Clock frequency: 200 MHz (ST and Renesas)
Clock source : HSE (ST) / PLL (Renesas)
date & time, sector cache, Fat cache size, threadx timer, Filex libraries
Start
File size 25 KB
Scheduler, tasks, priorities
RTOS mode: Filex w/ USB disk memory
STM32H573xx (CM33) vs RA6M5 (CM33)
USB host (MCU) identify, assign address and configure USB
device (USB disk)

## Slide 14: ST Competitors MW Benchmark: File System ST vs Renesas Tests
Renesas uses more complex structures and sets more variables, which improves code readability but increases RAM usage.
 | STM32H743ZI | RA8M1 | ST vs RA | Comment
Initialize | 258 | 331 | -22% | 
Create | 10 928 | 12 015 | -9% | 
Write | 1 374 020 | 1 505 481 | -9% | 
Read | 4 906 | 7 273 | -33% | 
BareMetal mode: Filex w/ SRAM internal memory
STM32H743xx (CM7) vs RA8M1 (CM85)
Execution time (CPU cycle)
Footprint (Bytes)
RTOS mode: Filex w/ USB disk memory
STM32H573xx (CM33) vs RA5M6 (CM33)
Although Renesas Cortex CM85 is more performer than STM32 Cortex CM7, STM32H7 is better than RA8M1 in file operations execution time w/ internal memory.
 | STM32H573xx | RA6M5 | ST vs RA | Comment
Initialize | 315 | 445 | -29% | 
Create | 400 705 | 213 446 | +88% | 
Write | 56 294 806 | 40 184 333 | +41% | 
Read | 3 996 239 | 3 917 021 | +2% | Almost equal
Execution time (CPU cycle)
 | STM32H573xx | RA6M5 | ST vs RA | Comment
ROM | 80 383 | 111 036 | -28% | 
RAM | 108 109 | 142 928 | -24% | 
Total | 188 492 | 253 959 | -26% | 
Footprint (Bytes)
Although ST and Renesas products have the same Cortex CM33, Renesas is better performing w/ external memory than ST.
Renesas uses more complex structures and sets more variables, which improves code readability but increases RAM usage.
 | STM32H743ZI | RA8M1 | ST vs RA | Comment
ROM | 21 904 | 19 356 | +13% | 
RAM | 11 548 | 29 808 | -61% | 
Total | 33 452 | 49 164 | -32% | 

## Slide 15
Clock configuration
Initialize SD card
Format and Create a file
Is SDcard inserted?
Clock source : HSI (ST) / FIRC_48M (NXP)
Clock frequency: CM33: 150 MHz (ST and NXP)
Initialize FATFS
Write in the file
Read the file
Close the file
Start
Set up the FATFS to use with the SD card
Yes
No
BareMetal mode: FatFS w/ SD card
STM32U575xx (CM33) vs MCX-N9 XX (CM33)
ST Competitors MW Benchmark: File System
ST vs NXP Flowcharts
Clock configuration
Format and Create a file
FATFS initialization
Write in file
Read file
Close file
Start
Clock source : HSI (ST) / FIRC_48M (NXP)
Clock frequency: CM33: 150 MHz (ST and NXP)
Configure FATFS to use SRAM as storage
BareMetal mode: FatFS w/ SRAM internal memory
STM32U575xx (CM33) vs MCX-N9 XX (CM33)

## Slide 16: ST Competitors MW Benchmark: File System ST vs NXP Tests
 | STM32U575xx | MCX N94 | ST vs NXP | Comment
FatFS Init | 152 382 | 110 987 | +37% | 
Create | 12 482 | 11 606 | +7% | Close file operations execution time.
Write | 6762 | 7288 | -7% | 
Read | 3713 | 3628 | +2% | 
BareMetal mode: FatFS w/ SRAM internal memory
Execution time (CPU cycle)
 | STM32U575 | MCX N94 | ST vs NXP
ROM | 14 348 | 12 100 | +19%
RAM | 5 820 | 102 357 | -94%
Total | 20 168 | 114 457 | -82%
Footprint (Bytes)
BareMetal mode: FatFS w/ SD card
 | STM32U575xx | MCX N94 | ST vs NXP | Comment
FatFS Init | 141 630 059 | 238 607 778 | -41% | STM32 SD HAL driver performing better than NXP
SD Init | 18 952 807 | 75 002 047 | -75% | 
Create | 274 521 | 110 147 207 | -99% | 
Write | 470 696 | 4 517 148 | -89% | 
Read | 92 988 | 96 432 | -3% | 
Execution time (CPU cycle)
 | STM32U575x | MCX N94 | ST vs NXP
ROM | 29 351 | 29 746 | -1%
RAM | 8 733 | 6 738 | +30%
Total | 38 084 | 36 484 | +4.39%
Footprint (Bytes)
STM32U575xx (CM33) vs MCX-N9 XX (CM33)
STM32U575xx (CM33) vs MCX-N9 XX (CM33)
STM32U575xx (CM33) vs MCX-N9 XX (CM33)
STM32U575xx (CM33) vs MCX-N9 XX (CM33)
NXP RAM is allocated as a table and used in read and write operations
Close total footprint

## Slide 17: ST Competitors MW Benchmark: USB Objective Performance comparison
This benchmark analysis was based on projects available within the ST, Renesas, and NXP firmware packages. Some updates were made in main.c to align with a common application scenario.
Test | Test Description | Reference project | Modifications done
RTOS mode : USBX CDC device class STM32H573xx (CM33) vs RA6M5 (CM33) | The test allows to configure MCU STM32H573xx/ RA6M5 as a virtual COM port to enable serial communication between MCU and PC (host). The application echoes the same data back. USB library operations to be analyzed are: USB initialization, enumeration phase and data transmission | ST: STM32H573I-DK\Applications\USBX\Ux_Device_CDC_ACM | 
 |  | RA: USBX_pcdc_acm_ek_ra6m5_ep (available in ra6m5-example) | 
RTOS mode : USBX HID host class STM32H573xx (CM33) vs RA6M5 (CM33) | The test enables communication between MCU STM32H573xx/ RA6M5 and mouse allowing the host (MCU) to receive and process mouse input events (left, right, middle). USB library operations to be analyzed are: USB initialization, enumeration phase and data transmission | ST: STM32H573I-DK\Applications\USBX\Ux_Host_HID | 
 |  | RA: USBX_hhid_ek_ra6m5_ep (available in ra6m5-example) | 
RTOS mode : USBX MSC host class STM32H573xx (CM33) vs RA6M5 (CM33) | The test allows to configure MCU STM32H573xx/ RA6M5 as an USB Host to enable file operations on an USB mass storage device (Flash Disk) using file system library (FileX). USB library operations to be analyzed are: USB initialization, enumeration phase, write and read file. | ST: STM32H573I-DK\Applications\USBX\Ux_Host_MSC | 
 |  | RA: USBX_hmsc_ek_ra6m5_ep (available in ra6m5-example) | 
BareMetal mode : Native USB CDC device class STM32U575xx (CM33) vs MCX-N9 XX (CM33) | The test allows to configure MCU STM32U575xx/ MCX-N9 as a virtual COM port to enable serial communication between MCU and PC (host). The application echoes the same data back. USB library operations to be analyzed are: USB initialization, enumeration phase and data transmission and reception | ST: GitHub ST: STM32H747I-EVAL\Applications\USB_Device\CDC_Standalone | 
BareMetal mode : Native USB HID device class STM32U575xx (CM33) vs MCX-N9 XX (CM33) | The test configures device (MCU) as a mouse and enables cursor movement along the X-axis. USB library operations to be analyzed are: USB initialization, enumeration phase and data transmission | ST: GitHub ST: STM32H747I-DISCO\Applications\USB_Device\HID_Standalone | 
BareMetal mode : Native USB MSC Host class STM32U575xx (CM33) vs MCX-N9 XX (CM33) | The test allows to configure MCU as an USB Host to enable file operations on an USB mass storage device (Flash Disk) using file system library (FatFS). USB library operations to be analyzed are: USB initialization, enumeration phase, write and read file. | ST: GitHub ST: STM32H747I-DISCO\Applications\USB_Host\MSC_Standalone | 
Renesas
NXP
These performed analyses are in line with the defined test plan in slide2

## Slide 18: ST Competitors MW Benchmark: USB ST vs Renesas Flowcharts
Clock configuration
RTOS Kernel Start
USBx Init
USB enumeration
No
Is device inserted ?
If USB Receive data
USB transmit data
Yes
Yes
No
Start
USB host (PC) identify, assign address and configure USB device (MCU)
Clock source : HSE (ST) / PLL (Renesas)
Clock frequency: 200 MHz (ST and Renesas)
USB Clock (48 MHz), USB Device, CDC class, power USB module
RTOS mode : USBX CDC device class
STM32H573xx (CM33) vs RA6M5 (CM33)
USB CDC device class: USB communication device class allows devices to communicate with computers as serial ports or network interfaces.
Scheduler, tasks, priorities
RTOS mode : USBX HID host class
STM32H573xx (CM33) vs RA6M5 (CM33)
Clock configuration
RTOS Kernel Start
USBX Init
Transmit data
Is mouse inserted?
Mouse buttons state changed ?
Yes
No
Yes
No
USB enumeration
USB host (MCU) identify, assign address and configure USB device (mouse)
Start
Clock source : HSE (ST) / PLL (Renesas)
Clock frequency: 200 MHz (ST and Renesas)
Scheduler, tasks, priorities
USB Clock (48 MHz), USB Host, HID class, power USB module
USB HID host class: USB Human Interface Device allows humans to communicate with the PC through device as keyboards, mouse or touch screen.

## Slide 19: ST Competitors MW Benchmark: USB ST vs Renesas Tests
RTOS mode : USBX CDC Device class
STM32H573xx (CM33) vs RA6M5 (CM33)
RTOS mode : USBX HID host class
STM32H573xx (CM33) vs RA6M5 (CM33)
 |  | STM32H573xx | RA6M5 | ST vs RA | Comment
Initialize |  | 0.6 | 11.97 | -95% | 
Enumeration |  | 135.4 | 137.9 | -2% | Amlost equal
Data transmission | Input* | 0.00911 | 0.0092 | -1% | Amlost equal
 | Output** | 0.0092 | 0.0092 | 0% | Equal
Execution time (ms)
 | STM32H573xx | RA6M5 | ST vs RA | Comment
ROM | 33'276 | 40'816 | -18% | 
RAM | 18'830 | 65'690 | -71% | RA RAM: 28 KB of gaps
Total | 52'106 | 106'506 | -51% | 
Footprint (Bytes)
(*):Data entering the host PC via the virtual COM port
(**):Data sent from the host PC via virtual COM port
- Renesas uses more complex structures and sets more variables, which improves code readability but increases RAM usage.
- ST RO Data is lower by 95% than Renesas, this is mainly due to the following layers:
r_usb_cstd_rtos.c (RA HAL USB driver): 3824 bytes
Rm_usbx_pcdc_descriptor.c (RA MW USBX porting layer): 310 bytes
Pin_data.c (RA generated configurations file): 684 bytes
- ST RW data is lower by 71% than Renesas, this is mainly due to the gaps in RAM that is uninitialized memory sections between the reserved memory regions (ST 0-byte vs RA 28 KB)
 | STM32H573xx | RA6M5 | ST vs RA | Comment
Initialize | 0,97 | 1.99 | -51% | 
Enumuration | 60 | 8 | +650% | USBX UX_DEVICE_ADDRESS_SET_WAIT ( 50 ms)
Data transmission (button presses) | 0.075 | 0.071 | +5.6% | 
Execution time (ms)
 | STM32H573xx | RA6M5 | ST vs RA | Comment
ROM | 54'051 | 65'212 | -17% | 
RAM | 43'733 | 98'640 | -56% | 
Total | 97'784 | 163'852 | -40% | 
Footprint (Bytes)
RA bypasses USBX enumeration phase by rm_usbx_ports porting layer
vs ST uses USBX enumeration phase that uses UX_DEVICE_ADDRESS_SET_WAIT ( 50 ms) constant to wait after setting the device address
Renesas uses more complex structures and sets more variables, which improves code readability but increases RAM usage.

## Slide 20: ST Competitors MW Benchmark: USB ST vs Renesas Flowcharts | Tests
RTOS mode : USBX MSC host class
STM32H573xx (CM33) vs RA6M5 (CM33)
USB MSC host class: USB mass storage device class allows an USB device to be recognized by the host (PC) and facilitates file transfers between the host and the USB device.
Close the file
Clock configuration
RTOS Kernel Start
Filex Init
USBx Init
Create the file
Write 25 KB in the file
Read the file
Is USB flash inserted ?
Yes
No
enumeration phase
Start
USB Clock (48 MHz), USB Host, MSC class, power USB module
date & time, sector cache, Fat cache size, Filex libraries
Clock source : HSE (ST) / PLL (Renesas)
Clock frequency: 200 MHz (ST and Renesas)
Scheduler, tasks, priorities
 | STM32H573xx | RA6M5 | ST vs RA | Comment
Initialize | 2.7 | 5.97 | -56% | 
Enumuration | 63.05 | 6 | +950% | USBX UX_DEVICE_ADDRESS_SET_WAIT ( 50 ms)
Execution time (ms)
 | STM32H573xx | RA6M5 | ST vs RA | Comment
ROM | 80'383 | 124'520 | -35% | RA hmsc_thread_entry.c application file size 45 084 bytes RA r_usb_cstd_rtos.c HAL USB Driver size 7 516 bytes
RAM | 108'109 | 88'484 | +22% | ST app_azure_rtos.c file RW data size is 78 936 bytes (73% of total RW data) due to ux_host_byte_pool_buffer (70 KB)
Total | 188'492 | 213'004 | -11% | 
Footprint (Bytes)
 | STM32H573xx | RA6M5 | ST vs RA | Comment
Write | 0.2 | 0.3 | -33% * | 
Read | 0.25 | 0.55 | -63.63% * | 
Throughput (MB/s)
 | STM32H573xx | RA6M5 | ST vs RA | Comment
Write | 0.3 | 0.3 | 0% | 
Read | 0.63 | 0.55 | +14.5% * | 
Throughput (MB/s) w/ stm32h5xx_hal_hcd.c / HCD_HC_IN_IRQHandler() static function enhancement request submitted
Bugzilla Ticket 217913
By setting the channel status to USB_CH_RX_VALID, it becomes immediately ready to receive data again without delays.
(*) Throughput (MB/s): The higher the better
RA bypasses USBX enumeration phase by rm_usbx_ports porting layer
vs ST uses USBX enumeration phase that uses UX_DEVICE_ADDRESS_SET_WAIT ( 50 ms) constant to wait after setting the device address

## Slide 21: ST Competitors MW Benchmark: USB ST vs Renesas: Cube2 low footprint profiles optimization
After applying the Cube 2–inspired optimizations (USBX/FreeRTOS), STM32 Cube1 projects (USBX/ThreadX) shows a clear improvement in both footprint and startup performance versus Renesas across USBX classes.
The footprint optimization is especially effective on RAM, with substantial memory reductions and lower initialization time, while maintaining comparable or better code size in most cases.
These results suggest that aligning the software architecture and configuration with the Cube 2 approach helps eliminate unnecessary memory overhead and improves overall efficiency, particularly for CDC and HID.
MSC remains the most demanding class, but ST still achieves a significant reduction in total footprint and init time compared with Renesas.
 | STM32H573xx | ST vs Renesas First Configuration | ST vs Renesas Low Footprint Configuration
CDC Device | ROM | -18% | -26.40%
 | RAM | -71% | -67.18%
 | Init execution time (ms) | -95% | -95.45%
HID Host | ROM | -17% | -14.21%
 | RAM | -56% | -52.94%
 | Init execution time (ms) | -51% | -55.35%
MSC Host | ROM | -35% | -46.90%
 | RAM | +22% | -42.93%
 | Init execution time (ms) | -56% | -41.67%
USBX applications |  | STM32H573xx First Configuration | STM32H573xx Low footprint Configuration | Low Footprint Configuration vs First Configuration
CDC Device | ROM | 33260 | 33284 | 0.07%
 | RAM | 18,830 | 17,422 | -7.48%
 | Init execution time (ms) | 0.6 | 0.5 | -16.67%
HID Host | ROM | 54,095 | 52655 | -2.66%
 | RAM | 43,733 | 36,657 | -16.18%
 | Init execution time (ms) | 0.97 | 0.71 | -26.80%
MSC Host | ROM | 70480 | 70476 | -0.01%
 | RAM | 108,109 | 69,197 | -35.99%
 | Init execution time (ms) | 2.77 | 2.24 | -19.13%
By applying the same low footprint optimizations on Renesas projects (to keep same scenario), these latter have significant gain also, but STM32 ROM and RAM footprint still better than Renesas.

## Slide 22: ST Competitors MW Benchmark: USB ST vs NXP Flowcharts
BareMetal mode : ST/NXP USB Library USB HID device class
STM32U575xx (CM33) vs MCX-N9 XX (CM33)
BareMetal mode : ST/NXP USB Library CDC device class
STM32U575xx (CM33) vs MCX-N9 XX (CM33)
USB Device Init
Clock configuration
Is device inserted ?
USB enemeration
Send mouse report
Start
Yes
No
Clock source : HSI (ST) / FIRC_48M (NXP)
Clock frequency: CM33: 150 MHz (ST and NXP)
U5/ MCX-N9: USB Full Speed, USB Device, CDC class
H7/ RT1170: USB High Speed, USB Device, CDC class
USB host (PC) identify, assign address and configure USB device (MCU)
USB HID device class: USB Human Interface Device allows to enable communication between device (MCU) and host (PC).
Yes
No
Yes
No
Clock configuration
USB configuration
If USB Receive data
USB transmit data
Is device inserted ?
Start
USB enemeration
Clock source : HSI (ST) / FIRC_48M (NXP)
Clock frequency: CM33: 150 MHz (ST and NXP)
U5/ MCX-N9: USB Full Speed, USB Device, CDC class
H7/ RT1170: USB High Speed, USB Device, CDC class
USB host (PC) identify, assign address and configure USB device (MCU)
USB CDC device class: USB communication device class allows devices to communicate with computers as serial ports or network interfaces.
Notes: Project Description:
This project demonstrates the use of the USB Device HID class by configuring the microcontroller to function as a mouse. It sets communication between the host (PC) and the microcontroller (mouse) enabling cursor movement along the X-axis.

## Slide 23: ST Competitors MW Benchmark: USB ST vs NXP Tests
BareMetal mode : ST/NXP USB Library HID device class
BareMetal mode : ST/NXP USB Library CDC device class
Execution time (ms)
 | STM32U575xx | MCX-N94X | ST vs NXP | Comment
ROM | 17013 | 13549 | +25.5% | * STM32 RCC Clock config 4560 bytes * FSL clock config 1470 bytes
RAM | 3065 | 1 360 | +125% | 
Total | 20078 | 14909 | +34% | 
Footprint (Bytes)
Execution time (ms)
Footprint (Bytes)
 | STM32U575xx | MCX-N94X | ST vs NXP | Comment
Initialize | 10 | 5 | +100% | 
Enumeration | 319.1 | 321.1 | -1% | 
Data transmission | 0.0092 | 0.00921 | 0% | 
 | STM32U575xx | MCX-N94X | ST vs NXP | Comment
ROM | 16377 | 13728 | +19.30% | * STM32 RCC Clock config 4560 bytes * FSL clock config 1558 bytes
RAM | 2422 | 1702 | +42.30% | 
Total | 18 799 | 15430 | +21% | 
STM32U575xx (CM33) vs MCX-N9 XX (CM33): : USB FS/ With RCC
STM32U575xx (CM33) vs MCX-N94 XX (CM33): USB FS
STM32U575xx (CM33) vs MCX-N94X (CM33) : USB FS
STM32U575xx (CM33) vs MCX-N94X (CM33): USB FS/ With RCC
 | STM32U575xx | MCX-N94X | ST vs NXP | Comment
Initialize | 9,993 | 8,159 | +22% | 
Enumeration | 72 | 70.4 | +2% | 
Transmit data | 0.00945 | 0.0095 | -1% | 
Receive data | 0.0094 | 0.0094 | 0% | 
 | STM32U575xx | MCX-N94X | ST vs NXP | Comment
ROM | 12453 | 12087 | +3% | By removing clock configuration footprint, ST is higher by only 15% than NXP instead of 34%
RAM | 3065 | 1352 | +126% | 
Total | 15518 | 13439 | +15% | 
STM32U575xx (CM33) vs MCX-N94X (CM33): USB FS/ Without RCC
 | STM32U575xx | MCX-N94X | ST vs NXP | Comment
ROM | 11817 | 12282 | -3.79% | By removing clock configuration footprint, ST is higher by only 2.6% than NXP instead of 21%
RAM | 2422 | 1590 | +52% | 
Total | 14239 | 13872 | +2.6% | 
STM32U575xx (CM33) vs MCX-N9 XX (CM33): : USB FS/ Without RCC

## Slide 24: ST Competitors MW Benchmark: USB ST vs NXP Flowcharts | Tests
Clock source : HSI (ST) / FIRC_48M (NXP)
Clock frequency: CM33: 150 MHz (ST and NXP)
U5/ MCX-N9: USB Full Speed
H7/ RT1170: USB High Speed
USB Host, MSC class
Close the file
Clock configuration
USB configuration
Format and Create a file
Is flash disk inserted ?
FATFS initialization
Write in the file 20 MB
Read 20 MB
Start
Mount the flash disk
USB enumeration
Yes
No
USB host (PC) identify, assign address and configure USB device (USB Flash Disk)
BareMetal mode : ST/NXP USB Library MSC Host class
STM32U575xx (CM33) vs MCX-N9 XX (CM33)
USB MSC Host class: USB mass storage Host class allows to configure MCU as an USB Host MSC and enables communication between MCU (host) and USB Flash disk (device)
 | STM32U575 | MCX-N94X | ST vs NXP | Comment
Initialize | 112 | 100.03 | +12% | 
Enumeration | 31 | 38 | -18% | 
Execution time (ms)
 | STM32U575 | MCX-N94X | ST vs NXP | Comment
ROM | 35025 | 26177 | +33.80% | * STM32 RCC Clock config 7184 bytes * FSL clock config 1705 bytes
RAM* | 13556 | 11859 | +14.31% | 
Total | 48,581 | 38,036 | +27.72% | 
Footprint (Bytes)
Throughput (KB/s)
STM32U575xx (CM33) vs MCX-N9 XX (CM33): USB FS
STM32U575xx (CM33) vs MCX-9 XX (CM33): USB FS
 | STM32U575 | MCX-N94X | ST vs NXP | Comment
Write | 911 | 936 | -2.7% | Throughput: the higher the better
Read | 951 | 982 | -3% | 
STM32U575xx (CM33) vs MCX-N9 XX (CM33): USB FS/ with RCC
 | STM32U575 | MCX-N94X | ST vs NXP | Comment
ROM | 27841 | 24584 | +13.25% | By removing clock configuration footprint, ST is higher by only 14% than NXP instead of 27.7%
RAM* | 13556 | 11747 | +15.40% | 
Total | 41397 | 36331 | +14% | 
STM32U575xx (CM33) vs MCX-N9 XX (CM33): USB FS/ without RCC
(*) Heap = 0x2000, stack = 0x2000. Stack is subtracted from RAM footprint

## Slide 25: ST Competitors MW Benchmark: USB ST vs NXP Clock configuration
ST generally has a larger USB middleware footprint than NXP, with the biggest gap in RAM, especially for CDC.
When RCC code is excluded, the ROM difference becomes much smaller, showing that part of the gap comes from clock configuration layers rather than USB stack.
=> ST is close in ROM for HID, but still heavier in RAM across most classes.
USB Class | CDC |  | HID |  | MSC | 
STM32U575 Clock | ROM | RAM | ROM | RAM | ROM | RAM
stm32u5xx_hal_rcc | 3008 | 0 | 3008 | 0 | 3084 | 0
stm32u5xx_hal_rcc_ex | 1552 | 0 | 1552 | 0 | 4100 | 0
Total | 4560 | 0 | 4560 | 0 | 7184 | 0
MCX-N9 Clock | ROM | RAM | ROM | RAM | ROM | RAM
fsl_clock | 1152 | 8 | 1054 | 112 | 1141 | 112
clock_config | 310 | 0 | 392 | 0 | 284 | 0
fsl_reset | 0 | 0 | 0 | 0 | 168 | 0
Total | 1462 | 8 | 1446 | 112 | 1593 | 112
clock_config gap (%) | 311.90% | 0% | 315.35% | 0% | 450.97% | 0%

## Slide 26: Continuation Plan Proposal

## Slide 27: STM32 vs Competitors
Middleware Stack | Benchmark Scope: ST vs GigaDevice | Headline KPIs | HW Board | Effort estimation
USB Device | Measure USB device stack efficiency across HID, CDC, and MSC through footprint, initialization, enumeration, and transfer performance. | Total footprint Initialization time Enumeration time Transfer latency | GD32E507Z-EVAL vs STM32U5A9J-DK Cortex: same M33 Frequency: 180 MHz vs 160 MHz Flash: 512 KB vs 4 MB SRAM: 128 KB vs 2.5 MB | 5 MD
FreeRTOS | Measure RTOS responsiveness and scalability through task, sync, queue, timer, ISR wakeup, and context-switch performance. | Total footprint Context-switch cost ISR wakeup latency API latency |  | 5 MD
FatFS | Measure file-system efficiency on external and removable storage through mount, format, and file operation performance. | Total footprint mount/format time File operations latency throughput |  | 5 MD
LwIP | Measure Ethernet stack efficiency through startup, network service latency, socket performance, and TCP/UDP throughput. | Total footprint Bring-up time TCP/UDP throughput |  | 7 MD
(*) estimation based on tests first development will be done by Copilot + Manual configuration adjustment and validation on HW boards
Benchmark Scope: Cube2 STM32C5 vs TI MSPM33 | HW Board
Done before on STM32C0 vs TI MSPM0. Now, we will assess changes in M33 products. STEP 1 Static analysis: Ecoystem, tools, drivers' architecture, … will be studied STEP 2 Functional analysis: LL equivalent scenarios deployment on STM32C5 and MPSM33 to evaluate footprint MW equivalent scenarios deployment on STM32C5 and MPSM33 to evaluate footprint and execution time (stacks to be defined) | MSPM33C321A vs STM32C5A3ZJ-NUCLEO Cortex: same M33 Frequency: 160 MHz vs 144 MHz Flash: same 1 MB SRAM: same 256 KB

## Slide 28: STM32 vs Renesas
Middleware Stack | Benchmark Scope | Headline KPIs | HW Board | Effort estimation*
FreeRTOS | Assess low-footprint multitasking efficiency for entry-class MCUs by measuring task lifecycle cost, API latency, and context-switch overhead under controlled scheduling conditions. | Total footprint API latency context-switch cost | FPB-RA0E1 vs NUCLEO‑STM32L031 Cortex: M23 vs M0+ Frequency: same 32 MHz Flash: 64 KB vs 32 KB SRAM: 12 KB vs 8 KB | 4 MD
LevelX | Evaluate persistent storage efficiency and flash-management readiness through format, mount/remount, and small-file create/delete cycle performance. | Total footprint Mount/remount time read/write throughput | EK-RA8M1 vs STM32H753 Cortex: M85 vs M7 Frequency: same 480 MHz Flash: same 2MB dual bank SRAM: same 1MB | 10 MD
USB | Compare USB stack footprint and class initialization performance across CDC, HID, and MSC by measuring initialization, enumeration, control-transfer latency, and transfer throughput. | Total footprint Initialization time enumeration time transfer throughput | FPB-RA8E1 vs NUCLEO‑STM32H743 Cortex: M85 vs M7 Frequency: 360 MHz vs 400 MHz Flash: 1MB vs 2 MB SRAM: 544 KB vs 1MB | 4 MD
(*) estimation based on tests first development will be done by Copilot + Manual configuration adjustment and validation on HW boards
Low priority

## Slide 29: STM32 vs NXP
Middleware Stack | Benchmark Scope | Headline KPIs | HW Board | Effort estimation*
FreeRTOS | Measure low-power M33 RTOS efficiency through task management, synchronization, message queues, timers, wakeup/sleep transitions, and context-switch latency. | Total footprint API latency Context-switch cost Wakeup latency | FRDM-MCXA156 vs NUCLEO-L552ZE-Q Cortex: same M33 Frequency: 96 MHz vs 110MHz Flash: same 512 KB SRAM: same 256 KB | 4 MD
FatFS | Measure SD storage middleware efficiency through mount, format, file operations, and directory scan performance. | Total footprint mount/format time File operations latency throughput | MIMXRT1060-EVKC vs STM32H735G-DK Cortex: same M7 Frequency: 600 MHz vs 550 MHz Flash: flashless vs 2 MB SRAM: same 1 MB | 4 MD
USB Device | Measure USB FS device stack efficiency across CDC, HID, and MSC through initialization, enumeration, control-transfer, and transfer performance. | Total footprint Initialization time Enumeration time Transfer latency | FRDM-MCXA156 vs NUCLEO-L552ZE-Q Cortex: same M33 Frequency: 96 MHz vs 110MHz Flash: same 512 KB SRAM: same 256 KB | 3 MD
LwIP | Measure Ethernet stack efficiency through startup, network service latency, socket performance, and TCP/UDP throughput. | Total footprint Bring-up time TCP/UDP throughput | MIMXRT1060-EVKC vs STM32H735G-DK Cortex: same M7 Frequency: 600 MHz vs 550 MHz Flash: flashless vs 2 MB SRAM: same 1 MB | 9 MD
(*) estimation based on tests first development will be done by Copilot + Manual configuration adjustment and validation on HW boards
Low priority

## Slide 30: Annex
Document/ SW Package | Owner | Link
Real-Time Operating System (RTOS) 2024 Performance Report | Jacob Beningo | RTOS 2024 Performance Report
STM32CubeU5 V1.8.0 | STMicroelectronics | STM32CubeU5
STM32CubeH5 V1.5.0 | STMicroelectronics | STM32CubeH5
STM32CubeH7 V1.12.0 | STMicroelectronics | STM32CubeH7
STM32CubeC0 V1.4.0 | STMicroelectronics | STM32CubeC0
stm32u5-classic-coremw-apps | STMicroelectronics | stm32u5-classic-coremw-apps
ra6m5-example 6.0.0 | Renesas | ra6m5-example
ra8m1-example 6.0.0 | Renesas | ra8m1-example
MCX-N9 XX 25_06_00 | NXP | MCUXpressoSDKBuilder
i.MX RT1170 25_06_00 | NXP | MCUXpressoSDKBuilder
MSPM0-SDK 2.06.00.05 | Texas Instrument | MSPM0-SDK

## Slide 31
Find out more at www.st.com

## Slide 32
For further support in creating a PowerPoint presentation, including graphic assets, formatting tools and additional information on the ST brand
you can visit the ST Brand Portal https://brandportal.st.com

## Slide 33: ST Competitors MW Benchmark: USB ST vs Renesas after optimization inspired from cube 2 Tests
RTOS mode : USBX CDC Device class
STM32H573xx (CM33) vs RA6M5 (CM33)
RTOS mode : USBX HID host class
STM32H573xx (CM33) vs RA6M5 (CM33)
 |  | STM32H573xx | RA6M5 | ST vs RA | Comment
Initialize |  | 0.5 | 11.98 | -95.74% | 
Enumeration |  | 135.4 | 137.9 | -2% | almost equal
Data transmission | Input* | 0.00911 | 0.0092 | -1% | almost equal
 | Output** | 0.0092 | 0.0092 | 0% | Equal
Execution time (ms)
 | STM32H573xx | RA6M5 | ST vs RA | Comment
RO code | 32,970 | 39466 | -16.46% | 
RO Data | 314 | 5,758 | -94.55% | 
RW Data | 17422 | 53,090 | -67.18% | RA RAM: 36 KB of gaps
Total | 50,706 | 98,314 | -48.42% | 
Footprint (Bytes)
(*):Data entering the host PC via the virtual COM port
(**):Data sent from the host PC via virtual COM port
- Renesas uses more complex structures and sets more variables, which improves code readability but increases RAM usage.
- ST RO Data is lower by 95% than Renesas, this is mainly due to the following layers:
r_usb_cstd_rtos.c (RA HAL USB driver): 3824 bytes
Rm_usbx_pcdc_descriptor.c (RA MW USBX porting layer): 310 bytes
Pin_data.c (RA generated configurations file): 684 bytes
- ST RW data is lower by 67% than Renesas, this is mainly due to the gaps in RAM that is uninitialized memory sections between the reserved memory regions (ST 0-byte vs RA 36 KB)
 | STM32H573xx | RA6M5 | ST vs RA | Comment
Initialize | 0.72 | 2.27 | -68.42% | 
Enumuration | 60 | 8 | +650% | USBX UX_DEVICE_ADDRESS_SET_WAIT ( 50 ms)
Data transmission (button presses) | 0.075 | 0.071 | +5.6% | 
Execution time (ms)
 | STM32H573xx | RA6M5 | ST vs RA |  | Comment
RO code | 53'374 | 54'930 | +1.75%% |  | allmost equal
RO Data | 677 | 10'282 | -93.53% |  | 
RW Data | 43'733 | 98'640 | -52.94% |  | 
Total | 97'784 | 163'852 | -35.87% |  | 
Footprint (Bytes)
RA bypasses USBX enumeration phase by rm_usbx_ports porting layer
vs ST uses USBX enumeration phase that uses UX_DEVICE_ADDRESS_SET_WAIT ( 50 ms) constant to wait after setting the device address
Renesas uses more complex structures and sets more variables, which improves code readability but increases RAM usage.

## Slide 34: ST Competitors MW Benchmark: USB ST vs Renesas Flowcharts | Tests
RTOS mode : USBX MSC host class
STM32H573xx (CM33) vs RA6M5 (CM33)
USB MSC host class: USB mass storage device class allows an USB device to be recognized by the host (PC) and facilitates file transfers between the host and the USB device.
Close the file
Clock configuration
RTOS Kernel Start
Filex Init
USBx Init
Create the file
Write 25 KB in the file
Read the file
Is USB flash inserted ?
Yes
No
enumeration phase
Start
USB Clock (48 MHz), USB Host, MSC class, power USB module
date & time, sector cache, Fat cache size, Filex libraries
Clock source : HSE (ST) / PLL (Renesas)
Clock frequency: 200 MHz (ST and Renesas)
Scheduler, tasks, priorities
 | STM32H573xx | RA6M5 | ST vs RA | Comment
Initialize | 2.24 | 4.85 | -53.77% | 
Enumuration | 63.05 | 6 | +950% | USBX UX_DEVICE_ADDRESS_SET_WAIT ( 50 ms)
Execution time (ms)
 | STM32H573xx | RA6M5 | ST vs RA | Comment
RO code | 69,8 | 70 174 | -0.53% | Allmost equal
RO Data | 674 | 62,54 | -98.92% | 
RW Data | 69,2 | 121,25 | -42.93% | 
Total | 139,67 | 253,964 | -45% | 
Footprint (Bytes)
 | STM32H573xx | RA6M5 | ST vs RA | Comment
Write | 0.2 | 0.3 | -33% * | 
Read | 0.25 | 0.55 | -63.63% * | 
Throughput (MB/s)
 | STM32H573xx | RA6M5 | ST vs RA | Comment
Write | 0.3 | 0.3 | 0% | 
Read | 0.63 | 0.55 | +14.5% * | 
Throughput (MB/s) w/ stm32h5xx_hal_hcd.c / HCD_HC_IN_IRQHandler() static function enhancement request submitted
Bugzilla Ticket 217913
By setting the channel status to USB_CH_RX_VALID, it becomes immediately ready to receive data again without delays.
(*) Throughput (MB/s): The higher the better
RA bypasses USBX enumeration phase by rm_usbx_ports porting layer
vs ST uses USBX enumeration phase that uses UX_DEVICE_ADDRESS_SET_WAIT ( 50 ms) constant to wait after setting the device address